## Slide 1
CB
SB
Hob.
Henderson Creek
Rangitopuni creek
Lucas creek

## Slide 2
Model validation
Surface velocity (Stanley Bay, SB; Charcoal Bay, CB)
Model Skill (Nash-Sutcliffe Efficiency, NSE. The closer to 1 the better) : 0.56 for velocity magnitude; 0.86 for the along-stream velocity component
Pearson’s R: 0.74 for velocity magnitude; 0.93 for the along-stream velocity component
Model Skill (Nash-Sutcliffe Efficiency, NSE. The closer to 1 the better) : 0.11 for velocity magnitude; 0.73 for the along-stream velocity component
Pearson’s R: 0.79 for velocity magnitude; 0.92 for the along-stream velocity component
Summary: 1. Along-stream velocity is well modelled; the challenge consists in improving the cross-stream component, which is notoriously difficult for estuarine models 2. For upstream locations near abrupt bathymetry changes, close to coastlines, e.g. CB, the result is not very satisfactory yet.

## Slide 3
Adding rivers to the model (on-going);
28th/Apr: salinity transect
Salinity validation at Hobsonville
Depth Averaged Salinity
Still some problems. (1) Hard to find or design an initial salinity field; (2) under-estimated upstream-downstream salinity gradient; (3) unsatisfactory drifter-tracking results (problems with residual currents?)